## Slide 1: Explainable Network Verification via Subspecifications User Study - Introduction of Background Knowledge

## Slide 2: Background: Explainable Network Verification
Network verifiers often give YES/NO (with a counterexample) answers, without explaining why.
Example: suppose we want a BGP policy blocking the private prefix 192.168.0.0/16.
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 12
2 !
3 ip prefix-list private_ips_2 seq 5 permit 192.168.0.0/16 ge 16
However, private_ips_2 is more precise than private_ips_1.
Overly restrictive filter may block more prefix than necessary.
Both of them pass the verification.

## Slide 3: Explainable Network Verification
Why a specific field, line, or block of the configuration satisfies the specification?
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 12
2 !
3 ip prefix-list private_ips_2 seq 5 permit 192.168.0.0/16 ge 16
permit
prefix cover 192.168.0.0/16
prefix ge range = 0~16
permit AND prefix cover 192.168.0.0/16 AND
prefix ge range = 0~16
private_ips_2 is the more precise option.
Both of them pass the verification.

## Slide 4: Explainable Network Verification via Subspecifications
Localized Subspecifications (Subspecs): the safe modification scope of that field, line, or block, while preserving the prior verification success.
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 12
2 !
3 ip prefix-list private_ips_2 seq 5 permit 192.168.0.0/16 ge 16
prefix ge range = 0~16
(>= 16 VAR_START)
prefix cover 192.168.0.0/16
(= ((_ extract 31 16) |0_dst-ip|) #xc0a8) AND
(= (bvnot (bvor (bvnot |0_dst-ip|) (bvnot VAR_MASK))) (bvnot (bvor (bvnot VAR_IP) (bvnot VAR_MASK))))
permit
(= VAR_ACTION true)
permit AND prefix cover 192.168.0.0/16 AND
prefix ge range = 0~16
(= ((_ extract 31 16) |0_dst-ip|) #xc0a8) AND
(= VAR_ACTION true) AND (>= 16 VAR_START) AND
(= (bvnot (bvor (bvnot |0_dst-ip|) (bvnot VAR_MASK))) (bvnot (bvor (bvnot VAR_IP) (bvnot VAR_MASK))))

## Slide 5: How to use subspec
Modification within subspec: preserves the verification property.
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 18
Modification out of subspec: may violate the property.
(sound but not complete)
prefix ge range = 0~16
(>= 16 VAR_START)
prefix ge range = 0~16
(>= 16 VAR_START)
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 14

## Slide 6: How to use subspec
Empty line-level subspec: can directly remove that line.
(or a line contains only a single subspec and the subspec is empty field-level subspec)
Empty subspec: can modify to anything.
empty
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 14
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 12
empty

## Slide 7: Tips for User Study
1. In this user study, we consider two granularities: field-level and line-level subspecs.
2. In this user study, the eBGP route selection process only involves AS-path length.
3. In this user study, the route-map naming rule is Router_Direction(IN_FROM/OUT_TO)_Peer.

## Slide 8: Explainable Network Verification via Subspecifications User Study - Introduction of Background Knowledge
Thank you for participating in this user study！

## Slide 9: Tips for Subspecs
1. modifications satisfying the subspec bounds are guaranteed to preserve the verified specifications
2. modifications exceeding the subspec bounds may violate the verified specifications (sound but not complete)
1 ip prefix-list private_ips_1 seq 5 deny 192.168.0.0/17 ge 17
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/16 ge 16
prefix cover 192.168.0.0/16
(= ((_ extract 31 16) |0_dst-ip|) #xc0a8) AND
(= (bvnot (bvor (bvnot |0_dst-ip|) (bvnot VAR_MASK))) (bvnot (bvor (bvnot VAR_IP) (bvnot VAR_MASK))))
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 12
prefix ge range = 0~16
(>= 16 VAR_START)
permit
(= VAR_ACTION true)
permit AND prefix cover 192.168.0.0/16 AND
prefix ge range = 0~16
(= ((_ extract 31 16) |0_dst-ip|) #xc0a8) AND
(= VAR_ACTION true) AND (>= 16 VAR_START) AND
(= (bvnot (bvor (bvnot |0_dst-ip|) (bvnot VAR_MASK))) (bvnot (bvor (bvnot VAR_IP) (bvnot VAR_MASK))))

## Slide 10: Tips for Empty Subspecs
1. safely modify that field with empty subspec without breaking the verified specifications
2. safely remove that line with empty line-level subspec without breaking the verified specifications
(or a line contains only a single field-level subspec and the field-level subspec is empty)
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 12
1 ip prefix-list private_ips_1 seq 5 deny 0.0.0.0/0 ge 0
1 ip prefix-list private_ips_1 seq 5 permit 192.168.0.0/12 ge 12
empty
empty
empty
empty